## Slide 1: A Node and Load Allocation Algorithm for Resilient CPSs under Energy-Exhaustion Attack
Tam Chantem and Ryan M. Gerdes
Electrical and Computer Engineering
Utah State University
Logan, UT 84322, USA

## Slide 2: Cyber-Physical Systems (CPSs)
Large complex systems
Tight coupling among computation, communications, and physical components
Many requirements
  Efficiency
  Security
  Timeliness
  Dependability
  Availability
  …

## Slide 3: Target Application
Outdoor tactical border surveillance system
Batteried nodes
  Detect motion
  Capture images
Specific requirements
  Save energy (solar)
  Deliver data in a timely manner

## Slide 4: Our Goal
To provide increased resilience to CPSs while under attack by
  Meeting real-time performance requirements
  Saving energy
Focus is on post attack resilience

## Slide 5: Existing Work
Plenty of research in CPS + security
  Stajano and Anderson
    Workshop on security and protocols, 1999
  Wang et al.
    IGCC, 2010
Some address real-time aspects
  Lin et al.,
    IEEE Trans. Industrial Informatics, 2009
  Lindberg and Arzen
    RTSS, 2010
  Xie and Qin
    IEEE Trans. Computers, 2006
Gap in knowledge: what to do once attacks occur?

## Slide 6: Energy-Exhaustion Attack
Drain nodes of their energy supplies
Increase node’s workloads
  Nodes may need to operate at higher speed levels
Can cause
  Temporal overloads
  Decreased performance
  Deadline misses
  Shortened lifetime
Observation: Nodes can still reliably execute the real-time tasks

## Slide 7: Problem Statement
Given
  A CPS with a number of nodes
    Some of which may be compromised
  Some specific CPS performance requirements
Perform
  Node allocation
    (Which nodes to assign real-time workloads to)
  Load allocation
    (How much workload to assign to a given node)
Such that
  Performance requirements are met
  Total remaining CPS energy is maximized
Approximate CPS lifetime

## Slide 8: CPS Model
|M| heterogeneous nodes
A node may be on or off
A live node executes a set of real-time tasks
  Total utilization and tasks to be executed determined by the node and load allocation process
EDF is used for task scheduling

## Slide 9: Node Energy Model
Each node runs on a battery and has energy-harvesting capability
Dynamic voltage and frequency (DVFS) scaling is used
  Referred collectively as speed level
  Normalized to [0, 1]
Remaining energy of a node at time t is
Current energy
Energy to run real-time tasks
Energy due to attack
Energy from recharging

## Slide 10: Energy-Exhaustion Attack Model
Detection mechanism based on the work by Mitchell and Chen (IEEE Trans. Reliability, 2013)
Each node is identified as compromised / uncompromised
  With false positive / negative rates
  With associated energy impact
    Via increase in speed level

## Slide 11: Proposed Approach
Formulate the node and load allocation problem as chance constrained problem
Use an efficient heuristic to solve the problem online

## Slide 12: Chance Constrained Program
Probabilistic formulation of a variation of the knapsack problem  Very difficult / time consuming to solve online

## Slide 13: Efficient Heuristic
Idea – use relative energy index of a given node mi as a basis for the algorithm
A node with a lower energy index is more efficient
  This also helps to compare heterogeneous nodes
Predicted power due to attack

## Slide 14: Heuristic Flow (1)
Utotal > |M|?
Utotal (workload)
Yes
No solution
Assign workload to nodes (next slide)
Predict attack impact on each node (if any)
Done
Yes
No
Has all the workload been assigned?
No

## Slide 15: Heuristic Flow (2)
Sort nodes lowest energy index first
More available nodes?
Can work be assigned to this node?
Assign work to this node
Yes
Yes
No
No
No Solution

## Slide 16: Properties of Heuristic
Time complexity of O(Uiter |M| log |M|)
  Uiter = Utotal / Ustep
  |M| is the number of nodes in the CPS
As Ustep  0, a solution will be found, if one exists
  How to set Ustep?

## Slide 17: Simulation Setup
Comparison points
  Algorithm A
    Sort nodes with largest remaining energy first
    Assign each node the maximum possible utilization in sorted order
  Algorithm B
    Similar to Algorithm A except utilization is incrementally assigned
Performance metrics
  Remaining CPS energy
  Number of dead nodes

## Slide 18: Results (1)
86% more live nodes
128 nodes, Ustep = 0.1

## Slide 19: Results (2)
128 nodes, Ustep = 0.1

## Slide 20: Results (3)
Compromised nodes: 25%, Ustep = 1
~99% more live nodes

## Slide 21: Results (4)
Compromised nodes: 25%, Ustep = 1

## Slide 22: Conclusions & Future Work
Promising results for continued operation post attack
  Judicious resource management
Food for thought
  Can we abstract the security part away?
  What to do if attacks are not resource-related?
  How much resources should we allocate to pre-attack / post-attack mechanisms for resilience?

## Slide 23: Thank you!
Questions?