## Slide 1: Task adaptation IN real-time & embedded systems FOR ENERGY & RELIABILITY TRADEOFFS
Sathish Gopalakrishnan
Department of Electrical & Computer Engineering
The University of British Columbia
sathish@ece.ubc.ca

## Slide 2
Why should we care about task adaptation in embedded systems?

## Slide 3: Intermittent Faults
40% of the real-world failures in a processor caused by intermittent faults [Nightingale et al., Eurosys 2011]
SDB
NBTI
Electromigration
HCI
Notes: Add manufacturing defects and design errors.

## Slide 4: Characterization
Intermittent errors are a serious concern, we need to know more about them.
  How do they affect programs?
  What are the properties of effective error tolerance techniques?

## Slide 5: Characterization: Fault Model
Length (tL)
Active duration (tA)
Location (unit)
Microarchitectural model
tL
tA
tI
Fault Mechanism | Gate-level models | Microarchitectural modelling
Gate-oxide breakdown | Intermittent delay | Intermittent stuck-at-last-value
Negative bias temperature instability | Intermittent delay | Intermittent stuck-at-last-value
Hot carrier injection | Intermittent delay | Intermittent stuck-at-last-value
Electromigration | Intermittent delay Intermittent open Intermittent short | Intermittent stuck-at-last-value Intermittent stuck-at-zero/one Dominant-0/1 bridging
Manufacturing defects | Intermittent open Intermittent short | Intermittent stuck-at-zero/one Dominant-0/1 bridging

## Slide 6: Characterization: Experimental Setup
We used the SPEC2006 benchmark suite.
Modify Microarchitectural-level simulator.
6
Microarchitectural Simulator
+
Fault Model
Crash
Fault start
Crash Distance
Error Propagation Set
6

## Slide 7: Characterization: Experimental Setup
We used the SPEC2006 benchmark suite.
Modify Microarchitectural-level simulator.
Microarchitectural Simulator
+
Fault Model
Silent Data Corruption
Fault start
Program Output
Program End
7

## Slide 8: Characterization: Experimental Setup
We used the SPEC2006 benchmark suite.
Modify Microarchitectural-level simulator.
Microarchitectural Simulator
+
Fault Model
Benign Fault
Fault start
Program Output
Program End
8

## Slide 9: Characterization: Results
Between 41% and 63% led to program crashes.
96% of the crash-causing errors led to crash within 100K dynamic instructions.
  How do they affect programs?

## Slide 10: Characterization: Results
88% of the crash-causing errors corrupt <500 data values.
  How do they affect programs?
Intermittent errors have serious impact on programs and require diagnosis and recovery mechanisms.

## Slide 11: ON TO TASK ADAPTATION

## Slide 12: Real-time systems
Need to meet timing constraints:
  Typically in the form of deadlines;
  Often requires that tasks not exceed time budgets.
Real-time and embedded systems are resource-constrained:
  Limited processing power;
  Energy consumption.

## Slide 13: Transformations for resource-constrained systems
Program transformations that yield:
  Shorter execution times;
  Reduced energy consumption;
  Increased reliability.

## Slide 14: Traditional Program Transformation
Transformation
≡
.c
.c

## Slide 15: Non-Traditional Program Transformation
≅
Transformation
.c
.c

## Slide 16: Loop Perforation of Motion Estimation in x264
Reference Frame
Current Frame
?
(Misailovic, et al.)
Notes: Most loops that we were able to identify were in the subcomputation that performs motion estimation.
Motion estimation is the technique instrumental for video compression. It matches similar blocks on both current and reference frame. For example if we want to identify the swimmer in the reference frame, the motion estimator compares different parts of the reference frame. The position of the surfer might have changed, either due to the movement of the surfer, or of the camera. After comparing with multiple blocks on a reference frame, the most similar block is selected. The part of the reference frame that best matches the current frame is finally selected.
-------------------
Motion estimation: describe the transformation from one 2D image to another (wiki: http://en.wikipedia.org/wiki/Motion_estimation)
Encoder performs both intra- and inter- frame compression. For reference frames only intra-frame compression is performed (Consequently, they consume more space). When encoding the following frames, the encoders tries to find the differences from the reference frame. Motion estimation describes the difference between the parts (blocks) of two frames caused by the movement of bodies or the camera (pan/zoom/tilt). For example, when we want to find the position of the swimmer in the reference frame, we in general have to check different parts of the reference frame. Then the part of the reference frame that is the most similar to the swimmer is selected, and only the distance vector is stored, thus saving considerable space
=====================================================
**GOAL**
Explain what motion estimation is

## Slide 17: Loop Perforation
int motion_estimation(block_t[] blocks, int n)
{
int idx = 0, best = INT_MAX, num_iters = 0, i = 0;
while (i < n) {
int cur = compute_distance(blocks[i]);
if (cur < best) {
idx = i;
best = cur;
}
num_iters = num_iters + 1;
i = i + 1;
}
assert (0 <= idx < n);
return idx;
}

## Slide 18: Loop Perforation
int motion_estimation(block_t[] blocks, int n)
{
int idx = 0, best = INT_MAX, num_iters = 0, i = 0;
while (i < n) {
int cur = compute_distance(blocks[i]);
if (cur < best) {
idx = i;
best = cur;
}
num_iters = num_iters + 1;
i = i + 2;
}
assert (0 <= idx < n);
return idx;
}

## Slide 19: Loop Perforation
int motion_estimation(block_t[] blocks, int n)
{
int idx = 0, best = INT_MAX, num_iters = 0, i = 0;
while (i < n) {
int cur = compute_distance(blocks[i]);
if (cur < best) {
idx = i;
best = cur;
}
num_iters = num_iters + 1;
i = i + 4;
}
assert (0 <= idx < n);
return idx;
}

## Slide 20: Quality of Service Profiling
Automatically explore alternate versions
QoS model
Program
Input(s)
Time Profiler
Subcomputation Transformation
Quality of Service profiler
timing info
performance vs QoS info
Transformation Evaluation
Notes: This situation leads to the following quality of service profiling concept.
Quality of Service profiling explores the space of optimization opportunities by automatically generating potential program optimizations.
Specifically, we first find the time consuming subcomputations, the same way standard profilers do. We then automatically transform each such subcomputation, one at a time. The goal of the transformation is to increase the performance of the subcomputation, and it is allowable for the transformation to induce less accurate result.
We then execute each of the transformed programs, and measure the quality of service loss and the performance. We select those subcomputations which, when transformed, deliver good performance with acceptable quality of service losses. and present them to the developer as good candidates for manual optimization
As we can see, the key element of our technique is a transformation or set of transformations that we perform to obtain alternative subcomputations. In this talk we will present one such transformation...
First, we extend the standard profiling process
Second, we use the
As we can see, the crucial part of our technique is the automatic transformation. Now the major question is, what should our transformation look like?
==================
***GOAL***
Automatic generation of optimization opportunities
Exploration: program TRANSFORMATION Based <<--
ITERATIVE – arrows back ????
multiple boxes... –

## Slide 21: Reliability
Failures happen:
  Hardware errors;
  Software errors/bugs.
Many error detection and recovery techniques exist:
  Redundancy and replication;
  Recovery blocks;
  Memory bounds checking;
  …
Reliability mechanisms are considered expensive:
  Overheads!

## Slide 22: BIG IDEA: Combine program transformations for time savings with transformations for reliability.

## Slide 23: BIG IDEA: Combine program transformations for time savings with transformations for reliability AND Allow software developers to specify approximations in cases when they cannot be automatically inferred.

## Slide 24: Overview

## Slide 25: Framework
Compilation pass built using LLVM/clang;
Runtime built using userspace scheduler over Minix3.

## Slide 26: Compilation Pass
Multiple versions based on user-provided approximations (programming language annotations);
Synthesize reliability mechanisms automatically:
  Currently restricted to bounds checking and memory padding [1],
  Replicated memory allocation in the heap [2],
  And replicated execution (software-implemented fault tolerance) [3].
[1] Rx, SOSP 2005 (UIUC)
[2] Samurai, EuroSys 2008 (MSR)
[3] SIFT, DSN 2006 (Princeton)

## Slide 27: Runtime System

## Slide 28: Minix3 Architecture

## Slide 29: Evaluation
Primary interest: Runtime Overhead
  Minix3 context switch time ~1.2 microseconds.
  With the adaptation framework: ~2.7 microseconds.
    But this is only for every new instance of a (periodic) task;
    Or can control the time window for adaptation.

## Slide 30: Related Work
Program approximation, loop perforation, etc.: Rinard, et al. (MIT)
Programming by Optimization: Hoos et al. (UBC)
And others that I am not emphasizing.

## Slide 31: Conclusions
Enabled tradeoff between QoS and reliability;
Framework for performing optimization;
Overheads appear to be acceptable.
Verifiable systems?
Morpheus: Neo, sooner or later you're going to realize just as I did that there's a difference between knowing the path and walking the path.
The Matrix (1999)